## Slide 1: Anomaly Detection in Cyclone Preheater Data
A Data-Driven Approach to Operational Monitoring
Presented by: Mohd Athar Shoyeb

## Slide 2: Data Preparation
Raw data ingested from Excel including multiple sensor readings over time.
• Sensor columns converted to numeric with invalid entries handled via coercion.
• Missing data dropped to ensure integrity of model input.
• Final dataset dimensions: 376124 rows × 8 columns.

## Slide 3: Analysis Strategy
Selected 6 key features linked to operational performance.
• StandardScaler applied for normalization across different units.
• Isolation Forest applied with 1% contamination to detect anomalies.
• Detected 3762 anomalies across the dataset.
• Grouped anomalies into continuous periods using 5-minute time gap logic.

## Slide 4: Insights & Findings
Total abnormal periods identified: 1434.
• Major deviations observed in Cyclone Material Temp, Inlet Gas Temp, and Inlet Draft.
• Frequent spikes/dips indicate potential equipment instability or faults.
• Next slide highlights top anomaly periods.

## Slide 5: Top 3 Anomaly Periods
start_time | end_time | duration | count | feature
2019-08-02 10:25:00 | 2019-08-03 01:25:00 | 0 days 15:00:00 | 181 | Cyclone_Material_Temp
2019-08-02 10:25:00 | 2019-08-03 01:25:00 | 0 days 15:00:00 | 181 | Cyclone_Inlet_Gas_Temp
2019-08-02 10:25:00 | 2019-08-03 01:25:00 | 0 days 15:00:00 | 181 | Cyclone_Inlet_Draft

## Slide 6: Anomaly Visualization - Cyclone_Material_Temp
Red points indicate anomalies

## Slide 7: Anomaly Visualization - Cyclone_Inlet_Gas_Temp
Red points indicate anomalies

## Slide 8: Anomaly Visualization - Cyclone_Inlet_Draft
Red points indicate anomalies